## Slide 1
IF
ID
EX
MEM
WB
5-STAGE RISC-V PIPELINE
PERFORMANCE EVALUATION
OF CPI FOR DIFFERENT
INSTRUCTION MIXES
IN A RISC PROCESSOR
MES College of Engineering, Kuttippuram | Dept. of AI & Data Science
Mini Project Report | B.Tech AI & DS | 2025–2026
Guide: Sherik K. K., Assistant Professor, Dept. of AI & DS
01

## Slide 2
TEAM MEMBERS
Project Team
MES24AD — Batch 2024 | Dept. of Artificial Intelligence and Data Science
01
FATHIMA MINSHA
Register No: MES24AD019
02
FARHA FATHIMA
Register No: MES24AD014
03
FATHIMA HAFNA SHERIN
Register No: MES24AD018
04
FATHIMATH NAJA
Register No: MES24AD023
05
HASNA TK
Register No: MES24AD025
06
RIDHIN MUHAMMED
Register No: MES24AD039
02

## Slide 3
TABLE OF CONTENTS
Overview
Topics covered in this presentation
01
Introduction
CPI, pipelining, instruction mix concepts
02
System Architecture
5-stage RISC-V pipeline design & hazard types
03
Experimental Methodology
Program design & simulation setup
04
Program Descriptions
Arithmetic, Memory & Control-heavy programs
05
Experimental Results
CPI, IPC & cycle data from Ripes
06
Analysis & Conclusion
Hazard comparison, key findings & summary
03

## Slide 4
INTRODUCTION
What is CPI and Why Does It Matter?
Cycles Per Instruction — the core metric of processor performance
Instruction Pipelining
Multiple instructions execute simultaneously across IF, ID, EX, MEM, WB stages. Ideal CPI = 1.0 (one instruction per cycle).
CPI — Cycles Per Instruction
Average clock cycles to execute one instruction. Calculated as: CPI = Total Cycles ÷ Instructions Retired.
Instruction Mix
Proportion of arithmetic, memory, and control instructions varies by program. Each type interacts differently with the pipeline.
Project Objective
Measure how arithmetic-heavy, memory-heavy, and control-heavy programs differ in CPI on a 5-stage RISC-V pipeline using Ripes simulator.
04

## Slide 5
SYSTEM DESIGN
5-Stage Pipeline Architecture
RISC-V processor stages and their functions
IF
Instruction Fetch
Fetches next instruction from memory using Program Counter (PC).
ID
Instruction Decode
Decodes instruction, reads register values from register file.
EX
Execute
Performs ALU operations or computes memory addresses. Branch conditions evaluated here.
MEM
Memory Access
Reads from or writes to data memory. Active only for LW and SW instructions.
WB
Write Back
Writes computed results back to destination register, completing the instruction.
SIMULATION CONFIGURATION
Simulator
Ripes — RISC-V Visual Simulator
Processor
5-Stage Pipeline (RV32IMC)
Hazard Handling
Data Forwarding + Pipeline Stalls
Memory Model
Harvard Architecture (separate I/D memory)
05

## Slide 6
PIPELINE HAZARDS
Instruction Mix vs. CPI Effect
How each instruction type impacts pipeline efficiency
ARITHMETIC
(ALU)
PIPELINE IMPACT
Executes in EX stage using registers only. No memory access.
STALL TYPE
Data Forwarding handles RAW hazards
EXPECTED CPI
Low ≈ 1.0–1.25
MEMORY
(Load/Store)
PIPELINE IMPACT
Requires MEM stage. Load-use hazards force pipeline stalls.
STALL TYPE
Load-use stall: 1 cycle per dependent load
EXPECTED CPI
Medium ≈ 1.5–1.62
CONTROL
(Branch/Jump)
PIPELINE IMPACT
Branch resolved in EX stage. Wrong-path instructions flushed.
STALL TYPE
Control flush: 1–2 cycles per taken branch
EXPECTED CPI
High ≈ 2.0–2.33
06

## Slide 7
PROGRAM 1 — ARITHMETIC
Arithmetic-Heavy Instruction Mix
16 instructions | ADD, SUB, MUL, DIV, ADDI — no memory, no branches
KEY CHARACTERISTICS
Register-to-register operations only: ADDI, ADD, SUB, MUL, DIV
No data memory access — zero LW/SW instructions
No branch or jump — completely sequential control flow
Data forwarding resolves most RAW hazards without stalls
16 instructions executed in 20 clock cycles
EXPECTED BEHAVIOR
Minimal pipeline stalls, efficient ALU utilization, and the lowest CPI among all three programs. Pipeline fills quickly and remains nearly full throughout execution.
07

## Slide 8
PROGRAM 1 — RESULTS
Arithmetic-Heavy: Simulation Output
Fig 2 — Ripes 5-Stage Processor Simulation
20
Total Clock Cycles
16
Instructions Retired
1.25
CPI (Cycles Per Instruction)
0.800
IPC (Instructions Per Cycle)
08

## Slide 9
PROGRAM 2 — MEMORY
Memory-Heavy Instruction Mix
13 instructions | LUI, LW, ADD, SW — array load-accumulate-store
KEY CHARACTERISTICS
Uses .data section: array .word 5, 10, 15, 20
Base address loaded using LUI + ADDI (hardware setup)
Four LW instructions each followed by dependent ADD — load-use hazards
One SW instruction stores final sum to memory
13 instructions in 21 cycles — load-use stalls add extra cycles
LOAD-USE HAZARD
Each LW → ADD pair forces a 1-cycle stall because loaded data isn't available until end of MEM stage, but forwarding can only go back to EX. Final x3 = 0x32 = 50 (5+10+15+20 ✔).
09

## Slide 10
PROGRAM 2 — RESULTS
Memory-Heavy: Simulation Output
Fig 4 — Ripes 5-Stage Processor Simulation
21
Total Clock Cycles
13
Instructions Retired
1.62
CPI (Cycles Per Instruction)
0.619
IPC (Instructions Per Cycle)
10

## Slide 11
PROGRAM 3 — CONTROL
Control-Heavy Instruction Mix
9 instructions | BEQ, BNE, BLT, BGE — maximum control hazards
KEY CHARACTERISTICS
Four different branch types: BEQ, BNE, BLT, BGE
Multiple labels: L1, L2, L3, L4 define branch targets
Each taken branch flushes 1–2 incorrectly fetched instructions
Control hazards dominate pipeline — branches = 44% of instruction stream
Only 9 instructions but 21 clock cycles — severe CPI degradation
EXPECTED BEHAVIOR
Highest CPI due to frequent pipeline flushes. Each taken branch discards partially-fetched instructions, causing repeated pipeline restart overhead.
11

## Slide 12
PROGRAM 3 — RESULTS
Control-Heavy: Simulation Output
Fig 6 — Ripes 5-Stage Processor Simulation
21
Total Clock Cycles
9
Instructions Retired
2.33
CPI (Cycles Per Instruction)
0.429
IPC (Instructions Per Cycle)
12

## Slide 13
EXPERIMENTAL RESULTS
CPI Comparison Across All Programs
Data recorded directly from Ripes Execution Info panel
ARITHMETIC
CYCLES
20
INSTRUCTIONS
16
CPI
1.25
IPC
0.800
EFFICIENCY
80%
FINAL REG
x16 = 0x9
MEMORY
CYCLES
21
INSTRUCTIONS
13
CPI
1.62
IPC
0.619
EFFICIENCY
62%
FINAL REG
x3 = 0x32
CONTROL
CYCLES
21
INSTRUCTIONS
9
CPI
2.33
IPC
0.429
EFFICIENCY
43%
FINAL REG
x3 = 0x1
Chart: 
| Arithmetic-Heavy | Memory-Heavy | Control-Heavy
CPI | 1.25 | 1.62 | 2.33
13

## Slide 14
RESULT ANALYSIS
Analysis & Discussion
Why each instruction mix performs differently
CPI COMPARISON
Arithmetic CPI = 1.25
80% efficiency — data forwarding resolves most RAW hazards
Memory CPI = 1.62
62% efficiency — 4 load-use stalls from LW→ADD patterns
Control CPI = 2.33
43% efficiency — branch flushes dominate (44% branch mix)
HAZARD TYPE SUMMARY
Arithmetic
Hazard: RAW (data)
Handling: Forwarding
CPI Impact: Low
Memory
Hazard: Load-Use
Handling: 1-cycle stall
CPI Impact: Medium
Control
Hazard: Branch flush
Handling: Pipeline flush
CPI Impact: High
KEY FINDING: Arithmetic CPI (1.25) < Memory CPI (1.62) < Control CPI (2.33) — Control-heavy programs are 86.4% slower than Arithmetic in terms of CPI
14

## Slide 15
CONCLUSION
Key Findings
CPI = 1.25
80% efficiency
Arithmetic-Heavy
Data forwarding resolves most RAW hazards. Near-ideal pipeline efficiency. Best-case CPI scenario.
CPI = 1.62
62% efficiency
Memory-Heavy
Load-use hazards cause 30% CPI increase. Each LW→ADD pair costs one extra stall cycle unavoidable by forwarding.
CPI = 2.33
43% efficiency
Control-Heavy
Branch flushes cause 86% CPI increase over arithmetic. Frequent pipeline restarts are the dominant bottleneck.
MES College of Engineering, Kuttippuram | Dept. of AI & DS | Mini Project 2025–2026 | Guide: Sherik K. K.
15

## Slide 16
IF
ID
EX
MEM
WB
THANK
YOU
for your attention
MES College of Engineering, Kuttippuram
Department of Artificial Intelligence and Data Science
Mini Project — B.Tech AI & DS | 2025–2026
Guide: Sherik K. K., Assistant Professor
Presented by:
Fathima Minsha
Farha Fathima
Fathima Hafna Sherin
Fathimath Naja
Hasna TK
Ridhin Muhammed
16

## Slide 17
Q
A
QUESTIONS &
ANSWERS
We welcome your questions!
MES College of Engineering, Kuttippuram | Dept. of AI & DS | 2025–2026
17